## Slide 1: Firewall Fundamentals

## Slide 2: Overzicht
Introduction to Firewall
Firewall Taxonomy
Firewall Architectures
Firewall Planning & Implementation
Firewall Limitations

## Slide 3: Introduction
Firewalls are devices or programs that control the flow of network traffic between networks or hosts that employ differing security postures.

## Slide 4: Introduction
What can firewalls do?
  Manage and control network traffic
  Authenticate access
  Act as an intermediary
  Protect resources
  Record and report on events (IDS, NIDS, IPS)
Firewalls operate at Layers 2, 3, 4, and 7 of the OSI model

## Slide 5
Firewall - A device or application that analyzes packet headers and enforces policy based on protocol type, source address, destination address, source port, and/or destination port. Packets that do not match policy are rejected.
Intrusion Detection System - A device or application that analyzes whole packets, both header and payload, looking for known events. When a known event is detected a log message is generated detailing the event.
Intrusion Prevention System - A device or application that analyzes whole packets, both header and payload, looking for known events. When a known event is detected the packet is rejected.

## Slide 6: Introduction
How does a firewall work?
deny/grant access based on the rules pre-defined by admin

## Slide 7: Taxonomy
FW Products
  Software
  ISA Server, Iptables, Comodo, ZoneAlarm,…
  Appliance
  Cisco PIX, Checkpoint, SonicWall, WatchGuard,…
  Integrated
  Multiple security functions in one single appliance: FW, IPS, VPN, Gateway Anti-virus/spam, data leak prevention…
Open vs. Closed Source FWs
  ipfw, ModSecurity, pfSense,…

## Slide 8: Taxonomy (classificatie)
FW Technologies
  Host-based (or Personal) FW
  Windows FW, Firestarter,…
  Network FW
    (Simple) Packet Filtering monitor in/out packets ip addresses (headers)
    Stateful Inspection app layer. dynamic
    Application FWs
    Application-Proxy Gateways
    Dedicated Proxy Servers NAT, cache, block sites, ..
    Transparent (Layer-2) FWs https://www.cisco.com/c/en/us/td/docs/ios-xml/ios/sec_data_zbf/configuration/xe-3s/sec-data-zbf-xe-book/zbfw-l2-transp-fw.pdf

## Slide 9: Taxonomy
FW Technologies
  Others (Network FW)
    NAT (it is actually a routing technology)
    VPN
    Network Access Control/Protection (NAC/NAP)
    Web Application FW
    Firewalls for Virtual Infrastructures
    Unified Threat Management (UTM)

## Slide 10: Architectures
DMZ
  Single (Three legged) firewall
Firewall

## Slide 11: Architectures
DMZ
  Dual firewall
External FW
Internal FW

## Slide 12: Planning & Implementation
Plan
Configure
Test
Deploy
Manage

## Slide 13: Limitations
What a firewall CAN’T protect against:
  viruses/malwares
  internal threats (disgruntled workers, poor security policy…)
  attacks that do not traverse the firewall (social engineering, personal modems or unauthorized wireless connections…)
  attacks on services that are allowed through the firewall (HTTP, SMTP, FTP…)

## Slide 14: Conclusion
Firewalls are an integral part of any Defense in Depth strategy

## Slide 15: References
[1] Firewall Fundamentals, Cisco Press (2006)
[2] Tactical Perimeter Defense, Element K (2007)
[3] Module 16 of CEH v7, EC-Council (2010)
[4] Building Internet Firewalls 2nd Edition, O'Reilly (2000)
[5] Guidelines on Firewalls and Firewall Policy, NIST (2009)